## Slide 1: Anytest: Localizing the Root Cause of Hardware Transport Performance Anomalies
Zhaochen Zhang, Jiaqi Gao, Sheng Cheng, Peiwen Yu, Feiyang Xue, Chang Liu, Boliang Liu, Kun Liu, Yubin Li, Rui Li, Li Wang, Peirui Cao, Qingkai Meng, Guihai Chen, Gang Lu, Bo Shi, Shuguang Cheng, Shu Ma, Yongqing Xi, Binzhang Fu, Dennis Cai, Chen Tian

## Slide 2: Offloading: performance gain and debugging pain.
Sender
tcp_cubic.c
Switch
sch_codel.c
Receiver
tcp_input.c
Sender
Blackbox hw. logic
Switch
Receiver
Blackbox hw. logic
Blackbox hw. logic
Software Network Stack
RDMA Network Stack
Offloading
Fast & near-zero CPU overhead!

## Slide 3: It’s easy to detect the problem, but hard localize it.
Packet
Loss!
Monitor
User
NPA Diagnosis
RDMA actions
Other Senders
Congestion
Control
Sender NIC
Switch
CNP
Reply
Receiver NIC
Loss
ECN marking
×
CNP interval
RDMA-tracer
Trace application
behavior
Localization
Repro. cases
Is ECN ignored?
Is CNP interval
too large?
Is bandwidth
sched. unfair?
Is max queue
length too short?
Is ECN mark
too fewer?
Is CC too
aggressive?
Synapse
Reproduce
the NPA
Root cause
Fix or mitigation
NPA
Please see our paper for details of RDMA-tracer and Synapse, two of our internal tools.

## Slide 4: Current counter-based monitor is coarse-grained
Transport reacts at sub-μs scale; counters aggregate over 10 ms – 1 s.
The same 10 ms counter value can produce 90–181 Gbps flow rate.
Aggregation erases the timing needed for diagnosis.

## Slide 5: RDMA network is tightly coupled
Other Senders
Congestion
Control
Sender NIC
Switch
CNP
Reply
Receiver NIC
Loss
ECN marking
×
CNP interval
Is ECN ignored?
Is CNP interval
too large?
Is bandwidth
sched. unfair?
Is max queue
length too short?
Is ECN mark
too fewer?
Is CC too
aggressive?
Sender, switch, and receiver form a closed feedback loop
Counters show correlation—not the responsible RP, NP, or CP
❓
❓

## Slide 6: Requirements of production-level localization tool
𝜇s- & packet-level resolution.
Event injection: Reproduce controlled anomaly triggers.
In-situ testing: Test the affected hardware in its production environment.
Method | Resolution Throughput Event . |  | Decompose | Inject | In-situ
Inference from counters | sec | Flow |  |  | 
Hardware testers | μs | Pkt |  |  | 
Test-suite generators | sec | Flow |  |  | 
Anytest (ours) | μs | Pkt |  |  | 
Decompose the interaction.

## Slide 7: Anytest: test the black box with white boxes
Hosts in production cluster
Functionality
DPDK emulator
White-box emulation
High precision measurement
Event injection
Target COTS Hardware
Black-box Logic
Standard RDMA verbs
Config
Result
Orchestrator
Env. setup
Start testing
Collection&Analysis
Key idea: surrounding the hardware with white-box software endpoints.

## Slide 8: Test each network role using specific scenarios
DPDK emulator (RP)
ACK/NACK/CNP
us-level record
DPDK emulator (RP)
ACK/NACK/CNP
us-level record
DPDK emulator (RP)
ACK/NACK/CNP
us-level record
Target COTS NIC (RP)
DPDK emulator (NP&CP)
Data Packet
ACK& CNP
Legacy / Programable CC
QoS
Tx Scheduling
ACK Reply
CNP Inject
us-level Tput & Pkt delay
DPDK emulator (CP)
Send Data Pkt
with ECN
Target COTS NIC (NP)
ACK/NACK Reply
CNP
Reply
DPDK emulator (RP)
ACK/NACK/CNP
us-level record
Data Pkt w/ ECN
ACK
NACK CNP
Please see CP test scenario in our paper……
RP Test Scenario
NP Test Scenario

## Slide 9: Catching the line rate
Dedicated threads isolate the critical datapath.
Lock-free SPSC rings preserve throughput and ordering.

## Slide 10: Catching the line rate
Pre-build invariant packet fields; update only the PSN at runtime.
Avoids per-packet allocation and payload initialization.
O(1) ICRC computation over the entire packet. See the paper for the algorithmic details

## Slide 11: Catching the line rate
Anytest can support 200 Gbps at 1 KB MTU, and 800 Gbps at 4 KB.

## Slide 12: AnyTest Production Deployment Workflow
Symptom Captured & Reproduced
Pick Track(s): CC / LR / Scheduling
Role-Isolated Regression Test
Find Failing Role/
Function Class?
Root Cause Localized
Sweep to Trigger
Yes—67.2% (automated)
On-Call Joint Localization
No—32.8%
iterate
codify the new test case into the regression suite (offline)
The only labor-intensive step
Anytest reduced the average localization effort to 3.1 person-hours per case

## Slide 13: Case study
Please see our paper for all representative cases……

## Slide 14: Conclusion
Thanks！
Find our open-source code at: https://github.com/AlibabaResearch/Anytest
Anytest is an in-situ, role-isolated black-box testing tool that turns RDMA root-cause localization into controlled experiments.
Fine-grained testing makes opaque, hardware-offloaded transports systematically diagnosable.
At Alibaba, Anytest localized 58 production NPAs, directly solved 67.2%, and reduced mean localization effort to 3.1 person-hours.